Matave Control Toolbox
Applied Control Engineering Toolbox for MATLAB and GNU Octave
Version 1.0
# Model building
Function name	Description	Status	MIMO	TF/SS	Discrete
tf	Crate transfer function model	Done	No	N/N	Y
zpk	Create zero-pole-gain model	Done	No	N/N	Y
ss	Create state space model	Done	Yes	N/N	Y

# Model transformation
Function name	Description	Status	MIMO	TF/SS	Discrete
Minreal	Minimal realization	Done	Yes	Y/Y	Y
Balreal	Balanced realization	Done	Yes	N/Y	Y
Modred	Model reduction	Done	Yes	N/Y	Y
Append	Append systems	Done	Yes	Y/Y	Y
Feedback	Feedback model	Done	Yes	Y/Y	Y
Series	Serial model	Done	Yes	Y/Y	Y
Parallel	Parallel model	Done	Yes	Y/Y	Y

# Model data access
Function name	Description	Status	MIMO	TF/SS	Discrete
dcgain	Get the low frequency gain	Done	Yes	Y/Y	Y
Pzmap	Plot poles and zeros	Done	Yes	Y/Y	Y
Damp	Get the damping	Done	Yes	Y/Y	Y
Pole	Get poles	Done	Yes	Y/Y	Y
zero	zeros for SISO	Done	No	Y/Y	Y
tzero	zeros for MIMO	Done	Yes	N/Y	Y

# Model conversions
Function name	Description	Status	MIMO	TF/SS	Discrete
C2d	Convert continuous to discrete	Done	Yes	Y/Y	N
C2dt	Convert continuous to discrete with delay	Done	Yes	Y/Y	N
D2c	Convert discrete to continuous	Done	Yes	Y/Y	Y
D2d	Rediscrete the model	Done	Yes	Y/Y	Y
Tf2ss	Transfer function to state space	Done	No	Y/N	Y
Ss2tf	State space to transfer function	Done	Yes	N/Y	Y

# Frequency domain analysis
Function name	Description	Status	MIMO	TF/SS	Discrete
evalfr	Get one frequency	Done	Yes	Y/Y	Y
freqresp	Get multiple frequencies	Done	Yes	Y/Y	Y
Bode	Bode diagram	Done	Yes	Y/Y	Y
Bodemag	Bode diagram without phase	Done	Yes	Y/Y	Y
Nyquist	Nyquist diagram	Done	Yes	Y/Y	Y
Sigma	Singular value diagram	Done	Yes	Y/Y	Y
Margin	Stability margins	Done	Yes	Y/Y	Y
Allmargin	Show all margin	Done	Yes	Y/Y	Y
Sensitivity	Show sensitivity margins	Done	Yes	Y/Y	Y
db2mag	Convert dB to magnintude	Done	Yes	Y/Y	Y
mag2db	Conver magnintude to dB	Done	Yes	Y/Y	Y
Rlocus	Root locus plot	Done	Yes	Y/Y	Y
dBdrop	Find the frequency at 3 dB drop	Done	Yes	Y/Y	Y

# Time domain analysis
Function name	Description	Status	MIMO	TF/SS	Discrete
gensig	Generate signals	Done	No	N/N	Y
Impulse	Impulse response	Done	Yes	Y/Y	Y
Step	Step response	Done	Yes	Y/Y	Y
Ramp	Ramp response	Done	Yes	Y/Y	Y
initial	Response with initial conditions	Done	Yes	N/Y	Y
Lsim	Linear simulation response	Done	Yes	Y/Y	Y

# Singel variable control
Function name	Description	Status	MIMO	TF/SS	Discrete
Pid	Parallel PID controller	Done	No	N/N	Y
PIPD	Serial PID controller	Done	No	N/N	Y
Loop	Loopshaping controller	Done	No	Y/N	Y
Acker	Acker formula	Done	No	N/Y	Y

# Multivariable control
Function name	Description	Status	MIMO	TF/SS	Discrete
lqr	Linear quadratic regulator	Done	Yes	N/Y	Y
lqe	Linear quadratic estimator	Done	Yes	N/Y	Y
Lqi	Linear quadratic integral	Done	Yes	N/Y	Y
reg	Generates the LQ-model	Done	Yes	N/Y	Y
Lqgreg	Generates the Gaussian LQG-model	Done	Yes	N/Y	Y

# Matrix equations
Function name	Description	Status	MIMO	TF/SS	Discrete
Lyap	Solve Lyapunov equation	Done	Y	N/Y	Y
are	Solve algibraic riccati equation	Done	Y	N/Y	Y
Obsv	Observbility matrix	Done	Y	N/Y	Y
Ctrb	Controllbility matrix	Done	Y	N/Y	Y
Gram	Gramian	Done	Y	N/Y	Y
Hsvd	Hankel singular values	Done	Y	N/Y	Y
Covar	Covaraiance matrix	Done	Y	N/Y	Y

# LQR + LQI:
Assume that we have a regular state space model
dot x = Ax + Bu newline y = Cx + Du
The LQR control law
u = -L x + Li x_i
with integral action LQI
alignl dot x_i = r - y = r - Cx - Du newline alignl x_i = int dot x_i =int (r - Cx - Du)
This will create the augmented state space model
left[ matrix{dot x## dot x_i} right ] = left [ matrix{A # 0 ## -C # 0} right ] left[ matrix{x## x_i} right ] + left [ matrix{B ## -D} right ]left[ matrix{u} right ] + left [ matrix{0 ## 1} right ]left[ matrix{r} right ] newline alignl y = Cx + Du
With the LQR and LQI control law. The augmented state space model will then be:
left[ matrix{dot x## dot x_i} right ] = left [ matrix{(A -BL) # BLi ## (DL-C) # -DLi} right ] left[ matrix{x## x_i} right ] + left [ matrix{0 ## 1} right ]left[ matrix{r} right ] newline alignl left [matrix{y} right] = left[ matrix{(C-DL) # DLi} right]left[ matrix{x## x_i} right ]

# LQR + LQE:
Assume a state space gaussian model
dot x = Ax + Bu + B_d d newline y = Cx + Du + B_n n
And a state state space gaussian observer
alignl dot hat x = A hat x + Bu + Ke newline alignl hat y = C hat x + Du newline alignl e = y - hat y = Cx + Du + B_n n - C hat x - Du = Cx + B_n n - C hat x
The LQR control law
u = -L x + r
One important step is to create one error state of diffrence between real state and estimated state
tilde x = x - hat x
This will change the control law to a new control law
u = -L hat x + r = L tilde x - L x + r
Because
tilde x - x= -hat x

Insert the new control law into the state space gaussian model
alignl dot x = Ax + B(L tilde x - L x + r) + B_d d newline alignl dot x = (A-BL)x + BL tilde x + Br + B_d d
Insert the new control law to the output of the state space gaussian model
alignl y = Cx + D(L tilde x - L x + r) + B_n n newline alignl y = (C - DL)x + DL tilde x + Dr + B_n n
Insert the new control law into the state state space gaussian observer
alignl dot hat x = A hat x + Bu + Ke newline alignl dot hat x = A hat x + B(L tilde x - L x + r) + K(Cx + B_n n - C hat x) newline alignl dot hat x = A hat x + BL tilde x -BL x + Br + KCx + KB_n n - KC hat x
Assume now
alignl dot tilde x = dot x - dot hat x newline alignl dot tilde x = [ (A-BL)x + BL tilde x + r + B_d d ] - [ A hat x + BL tilde x -BL x + r + KCx + KB_n n - KC hat x ] newline alignl dot tilde x = Ax - BLx + BL tilde x + r + B_d d - A hat x - BL tilde x + BL x - r - KCx - KB_n n + KC hat x newline alignl dot tilde x = Ax + B_d d - A hat x - KCx - KB_n n + KC hat x newline

Remember
tilde x = x - hat x
Which results:
alignl dot tilde x = Ax + B_d d - A hat x - KCx - KB_n n + KC hat x newline alignl dot tilde x = A(x - hat x) + B_d d - KC(x - hat x) - KB_n n newline alignl dot tilde x = ( A - KC ) tilde x + B_d d - KB_n n
The whole state space model will then be:
alignl left [matrix{dot x ## dot tilde x} right ] = left [ matrix{(A-BL) # BL ## 0 # (A-KC)} right ] left [ matrix{x ## tilde x} right ] + left [ matrix{B # B_d # 0 ## 0 # B_d # - KB_n} right ] left [ matrix{r ## d ## n} right ] newline alignl y = left [ matrix{(C-DL) # DL} right] left [ matrix{x ## tilde x} right ] + left [ matrix{Dr # 0 # B_n} right] left [ matrix{r ## d ## n} right ]
Because the most important equations are:
alignl dot x = (A-BL)x + BL tilde x + Br + B_d d newline alignl dot tilde x = ( A - KC ) tilde x + B_d d - KB_n n newline alignl y = (C - DL)x + DL tilde x + Dr + B_n n

# LQR + LQE + LQI:
Assume a state space gaussian model
dot x = Ax + Bu + B_d d newline y = Cx + Du + B_n n
And a state state space gaussian observer
alignl dot hat x = A hat x + Bu + Ke newline alignl hat y = C hat x + Du newline alignl e = y - hat y = Cx + Du + B_n n - C hat x - Du = Cx + B_n n - C hat x
The LQR control law
u = -L hat x + Li x_i
with integral action LQI
alignl dot x_i = r - y = r - Cx - Du - B_n n newline alignl x_i = int dot x_i =int (r - Cx - Du - B_n n)
One important step is to create one error state of diffrence between real state and estimated state
tilde x = x - hat x
This will change the control law to a new control law
u = -L hat x + Li x_i = L tilde x - L x + Li x_i
Because
tilde x - x= -hat x

Insert the new control law into the integral state
alignl dot x_i = r - y = r - Cx - D(L tilde x - L x + Li x_i) - B_n n newline alignl dot x_i = r - y = r - Cx - DL tilde x + DL x - DLi x_i - B_n n = r + ( DL - C )x - DL tilde x - DLi x_i - B_n n
Insert the new control law into the state space gaussian model
alignl dot x = Ax + B(L tilde x - L x + Li x_i) + B_d d newline alignl dot x = (A-BL)x + BL tilde x + BLi x_i + B_d d
Insert the new control law to the output of the state space gaussian model
alignl y = Cx + D(L tilde x - L x + Li x_i) + B_n n newline alignl y = (C - DL)x + DL tilde x + DLi x_i + B_n n
Insert the new control law into the state state space gaussian observer
alignl dot hat x = A hat x + Bu + Ke newline alignl dot hat x = A hat x + B(L tilde x - L x + Li x_i) + K(Cx + B_n n - C hat x) newline alignl dot hat x = A hat x + BL tilde x -BL x + BLi x_i + KCx + KB_n n - KC hat x
Assume now
alignl dot tilde x = dot x - dot hat x newline alignl dot tilde x = [ (A-BL)x + BL tilde x + BLi x_i + B_d d ] - [ A hat x + BL tilde x -BL x + BLi x_i + KCx + KB_n n - KC hat x ] newline alignl dot tilde x = Ax - BLx + BL tilde x + BLi x_i + B_d d - A hat x - BL tilde x + BL x - BLi x_i - KCx - KB_n n + KC hat x newline alignl dot tilde x = Ax + B_d d - A hat x - KCx - KB_n n + KC hat x newline
Remember
tilde x = x - hat x
Which results
alignl dot tilde x = Ax + B_d d - A hat x - KCx - KB_n n + KC hat x newline alignl dot tilde x = A(x - hat x) + B_d d - KC(x - hat x) - KB_n n newline alignl dot tilde x = ( A - KC ) tilde x + B_d d - KB_n n
The whole state space model will then be:
alignl left [matrix{dot x ## dot tilde x ## dot x_i} right ] = left [ matrix{(A-BL) # BL # BLi ## 0 # (A-KC) # 0 ## (DL-C) # -DL # -DLi} right ] left [ matrix{x ## tilde x ## x_i} right ] + left [ matrix{0 # B_d # 0 ## 0 # B_d # - KB_n ## 1 # 0 # -B_n} right ] left [ matrix{r ## d ## n} right ] newline alignl y = left [ matrix{(C-DL) # DL # DLi} right] left [ matrix{x ## tilde x ## x_i} right ] + left [ matrix{0 # 0 # B_n} right] left [ matrix{r ## d ## n} right ]
Because the most important equations are:
alignl dot x = (A-BL)x + BL tilde x + BLi x_i + B_d d newline alignl dot tilde x = ( A - KC ) tilde x + B_d d - KB_n n newline alignl dot x_i = r + ( DL - C )x - DL tilde x - DLi x_i - B_n n newline alignl y = (C - DL)x + DL tilde x + DLi x_i + B_n n