Linear Model Predictive Control
# 1: Create augmented model with integration
State space model – This is what you begin with.
alignl x_m (k+1) = A_m x_m( k ) + B_m u( k ) newline alignl y( k ) = C_m x_m( k )
Where:
alignl A_m in Re^nxn newline alignl B_m in Re^nxm newline alignl C_m in Re^qxn newline alignl o_m in 0^qxn newline alignl x_m in Re^n newline alignl y in Re^q newline alignl u in Re^m
Augmented state space model with internal integration
alignl left [ matrix{%DELTA x_m(k+1) ## y(k+1)} right ] = left[ matrix{A_m # o_m^T ## C_m A_m # I_{qxq} } right ] left [ matrix{%DELTA x_m(k) ## y(k)} right ] + left [ matrix{B_m ## C_m B_m} right ] %DELTA u( k ) newline alignl y( k ) = left [matrix{o_m # I_{qxq}} right ] left [ matrix{%DELTA x_m(k) ## y(k)} right ]
Where:
alignl %DELTA u( k ) = u( k ) - u( k-1 ) newline alignl %DELTA x_m(k) = x_m( k ) - x_m( k-1 ) newline alignl %DELTA x_m( k+1 ) = x_m( k+1) - x_m( k) newline

# 2: Create the prediction matrecies
Prediction equation.
Y = Fx( k_i ) + %PHI %DELTA U
F = left [ matrix{CA ## CA^2 ## CA^3 ## dotsvert ## CA^{N_p} } right ] , %PHI = left[ matrix{CB # 0 # 0 # dotsaxis # 0 ## CAB # CB # 0 # dotsaxis # 0 ## CA^2 B # CAB # CB # dotsaxis # 0 ## dotsvert # dotsvert # dotsvert # dotsvert # dotsvert ## CA^{N_p -1}B # CA^{N_p -2}B # CA^{N_p -3}B # dotsaxis # CA^{N_p -N_c}B}right ]
Where:
alignl A = left[ matrix{A_m # o_m^T ## C_m A_m # I_{qxq} } right ] newline alignl B = left [ matrix{B_m ## C_m B_m} right ] newline alignl C = left [matrix{o_m # I_{qxq}} right ] newline alignl x( k_i ) = left [ matrix{%DELTA x_m(k_i) ## y(k_i)} right ] (Current state) newline alignl N_p in Re ( Prediction horizon ) newline alignl N_c in Re ( Control horizon ) newline alignl k_i in Re ( Sampling step )
Future trajectories of inputs and outputs:
alignl %DELTA U = left [ matrix{%DELTA u(k_i) # %DELTA u(k_i + 1) # %DELTA u(k_i + 2) # dotsaxis # %DELTA u(k_i + N_c - 1)} right ]^T newline alignl Y = left [ matrix{y(k_i + 1 mline k_i) # y(k_i + 2 mline k_i) # y(k_i + 3 mline k_i) # dotsaxis # y(k_i + N_p mline k_i) } right ]^T
Where y(k_i + 1 mline k_i) is interprented as ”Predicted output variable at k_i + 1 with given current plant information position k_i ”.

# 3: Open loop MPC
Minimize the cost function and find the best input trajectories.
J = ( r(k_i) - Y )^T( r(k_i) - Y ) + %DELTA U^T bar R %DELTA U
This can be reformulated as:
J = ( r(k_i) - Fx(k_i) )^T( r(k_i) - Fx(k_i) ) -2 %DELTA U^T %PHI^T ( r(k_i) - Fx(k_i) ) + %DELTA U^T ( %PHI^T %PHI + bar R ) %DELTA U
And to minimize the derivative of J :
{ partial J } over { partial %DELTA U } = - 2 %PHI ^T ( r(k_i) - Fx(k_i)) + 2( %PHI^T %PHI + bar R ) %DELTA U = 0
And find the optimal input trajectories %DELTA U when J = 0 :
%DELTA U = ( %PHI^T %PHI + bar R )^{ -1 }%PHI^T( r(k_i) - Fx(k_i) )
Where:
alignl bar R = r_{ %omega } I_{ N_c x N_c } newline alignl r_{ %omega } >= 0 in Re ( Tuning parameter ) newline alignl r(k_i) in Re^{N_p} ( Set-point vector )
# 4: Closed loop MPC
Find the static control law.
%DELTA u( k_i ) = K_y r(k_i) - K_mpc x( k_i )
And create the closed loop MPC controller
alignl x(k_i+1) = left [matrix{(A-BK_mpc)} right ]x(k_i) + left [matrix{BK_y} right]r( k_i ) newline alignl y( k_i ) = Cx( k_i )
Where:
alignl K_y = {left [ matrix{I_{mxm} # I_{mxm} times 0 # I_{mxm} times 0 # dotsaxis # I_{mxm} times0} right ]} overbrace {N_c} ( %PHI^T %PHI + bar R )^{ -1 } %PHI ^T bar R_s newline alignl K_mpc = {left [ matrix{I_{mxm} # I_{mxm} times 0 # I_{mxm} times 0 # dotsaxis # I_{mxm} times0} right ]} overbrace {N_c} ( %PHI^T %PHI + bar R )^{ -1 } %PHI ^T F newline alignl bar R_s = {left [ matrix{1 # 1 # 1 # 1 # dotsaxis # 1} right ]}^T overbrace {N_p}

# 5: Closed loop MPC with kalman filter
Use mpcreg.m and get the kalman gain matrix from lqe.m function.