# Linear Quadratic regulators
# LQR + LQI:
Assume that we have a regular state space model
dot x = Ax + Bu newline y = Cx + Du
The LQR control law
u = -L x + Li x_i
with integral action LQI
alignl dot x_i = r - y = r - Cx - Du newline alignl x_i = int dot x_i =int (r - Cx - Du)
This will create the augmented state space model.
Also added precompensator vector BK_r where K_r >= 0,in Re^m, B in Re^nxm . That vector need to be specified from the user.
left[ matrix{dot x## dot x_i} right ] = left [ matrix{A # 0 ## -C # 0} right ] left[ matrix{x## x_i} right ] + left [ matrix{B ## -D} right ]left[ matrix{u} right ] + left [ matrix{BK_r ## 1} right ]left[ matrix{r} right ] newline alignl y = Cx + Du
With the LQR and LQI control law. The augmented state space model will then be:
left[ matrix{dot x## dot x_i} right ] = left [ matrix{(A -BL) # BLi ## (DL-C) # -DLi} right ] left[ matrix{x## x_i} right ] + left [ matrix{BK_r ## 1} right ]left[ matrix{r} right ] newline alignl left [matrix{y} right] = left[ matrix{(C-DL) # DLi} right]left[ matrix{x## x_i} right ]
This is what Matacecontrol is using.
# LQR + LQE: Also called LQG controller
Assume a state space gaussian model
dot x = Ax + Bu + B_d d newline y = Cx + Du + B_n n
And a state state space gaussian observer
alignl dot hat x = A hat x + Bu + Ke newline alignl hat y = C hat x + Du newline alignl e = y - hat y = Cx + Du + B_n n - C hat x - Du = Cx + B_n n - C hat x
The LQR control law
u = -L x + r
One important step is to create one error state of diffrence between real state and estimated state
tilde x = x - hat x
This will change the control law to a new control law
u = -L hat x + r = L tilde x - L x + r
Because
tilde x - x= -hat x

Insert the new control law into the state space gaussian model
alignl dot x = Ax + B(L tilde x - L x + r) + B_d d newline alignl dot x = (A-BL)x + BL tilde x + Br + B_d d
Insert the new control law to the output of the state space gaussian model
alignl y = Cx + D(L tilde x - L x + r) + B_n n newline alignl y = (C - DL)x + DL tilde x + Dr + B_n n
Insert the new control law into the state state space gaussian observer
alignl dot hat x = A hat x + Bu + Ke newline alignl dot hat x = A hat x + B(L tilde x - L x + r) + K(Cx + B_n n - C hat x) newline alignl dot hat x = A hat x + BL tilde x -BL x + Br + KCx + KB_n n - KC hat x
Assume now
alignl dot tilde x = dot x - dot hat x newline alignl dot tilde x = [ (A-BL)x + BL tilde x + r + B_d d ] - [ A hat x + BL tilde x -BL x + r + KCx + KB_n n - KC hat x ] newline alignl dot tilde x = Ax - BLx + BL tilde x + r + B_d d - A hat x - BL tilde x + BL x - r - KCx - KB_n n + KC hat x newline alignl dot tilde x = Ax + B_d d - A hat x - KCx - KB_n n + KC hat x newline
Remember
tilde x = x - hat x
Which results:
alignl dot tilde x = Ax + B_d d - A hat x - KCx - KB_n n + KC hat x newline alignl dot tilde x = A(x - hat x) + B_d d - KC(x - hat x) - KB_n n newline alignl dot tilde x = ( A - KC ) tilde x + B_d d - KB_n n
The whole state space model will then be: Also added precompensator factor K_r where K_r >= 0,in Re^m, B in Re^nxm . That factor is computed automaticly.
alignl left [matrix{dot x ## dot tilde x} right ] = left [ matrix{(A-BL) # BL ## 0 # (A-KC)} right ] left [ matrix{x ## tilde x} right ] + left [ matrix{BK_r # B_d # 0 ## 0 # B_d # - KB_n} right ] left [ matrix{r ## d ## n} right ] newline alignl y = left [ matrix{(C-DL) # DL} right] left [ matrix{x ## tilde x} right ] + left [ matrix{D # 0 # B_n} right] left [ matrix{r ## d ## n} right ]
Because the most important equations are:
alignl dot x = (A-BL)x + BL tilde x + Br + B_d d newline alignl dot tilde x = ( A - KC ) tilde x + B_d d - KB_n n newline alignl y = (C - DL)x + DL tilde x + Dr + B_n n

That was the deep theory!

But the state space model in Matavecontrol is:
alignl left [matrix{dot x ## dot tilde x} right ] = left [ matrix{(A-BL) # BL ## 0 # (A-KC)} right ] left [ matrix{x ## tilde x} right ] + left [ matrix{BK_r # B_d # 0 ## 0 # B_d # -KB_n} right ] left [ matrix{r ## d ## n} right ] newline alignl left[ matrix{y ## y_m ## u} right] = left [ matrix{C # 0 ## C # 0 ## -L # L} right] left [ matrix{x ## tilde x} right ] + left [ matrix{0 # 0 # 0 ## 0 # 0 # B_n ## K_r # 0 # 0} right] left [ matrix{r ## d ## n} right ]

Where y_m is the measured signal and y is the filtered output.
# LQR + LQE + LQI: (Not included in Matavecontrol)
Assume a state space gaussian model
dot x = Ax + Bu + B_d d newline y = Cx + Du + B_n n
And a state state space gaussian observer
alignl dot hat x = A hat x + Bu + Ke newline alignl hat y = C hat x + Du newline alignl e = y - hat y = Cx + Du + B_n n - C hat x - Du = Cx + B_n n - C hat x
The LQR control law
u = -L hat x + Li x_i
with integral action LQI
alignl dot x_i = r - y = r - Cx - Du - B_n n newline alignl x_i = int dot x_i =int (r - Cx - Du - B_n n)
One important step is to create one error state of diffrence between real state and estimated state
tilde x = x - hat x
This will change the control law to a new control law
u = -L hat x + Li x_i = L tilde x - L x + Li x_i
Because
tilde x - x= -hat x

Insert the new control law into the integral state
alignl dot x_i = r - y = r - Cx - D(L tilde x - L x + Li x_i) - B_n n newline alignl dot x_i = r - y = r - Cx - DL tilde x + DL x - DLi x_i - B_n n = r + ( DL - C )x - DL tilde x - DLi x_i - B_n n
Insert the new control law into the state space gaussian model
alignl dot x = Ax + B(L tilde x - L x + Li x_i) + B_d d newline alignl dot x = (A-BL)x + BL tilde x + BLi x_i + B_d d
Insert the new control law to the output of the state space gaussian model
alignl y = Cx + D(L tilde x - L x + Li x_i) + B_n n newline alignl y = (C - DL)x + DL tilde x + DLi x_i + B_n n
Insert the new control law into the state state space gaussian observer
alignl dot hat x = A hat x + Bu + Ke newline alignl dot hat x = A hat x + B(L tilde x - L x + Li x_i) + K(Cx + B_n n - C hat x) newline alignl dot hat x = A hat x + BL tilde x -BL x + BLi x_i + KCx + KB_n n - KC hat x
Assume now
alignl dot tilde x = dot x - dot hat x newline alignl dot tilde x = [ (A-BL)x + BL tilde x + BLi x_i + B_d d ] - [ A hat x + BL tilde x -BL x + BLi x_i + KCx + KB_n n - KC hat x ] newline alignl dot tilde x = Ax - BLx + BL tilde x + BLi x_i + B_d d - A hat x - BL tilde x + BL x - BLi x_i - KCx - KB_n n + KC hat x newline alignl dot tilde x = Ax + B_d d - A hat x - KCx - KB_n n + KC hat x newline
Remember
tilde x = x - hat x
Which results
alignl dot tilde x = Ax + B_d d - A hat x - KCx - KB_n n + KC hat x newline alignl dot tilde x = A(x - hat x) + B_d d - KC(x - hat x) - KB_n n newline alignl dot tilde x = ( A - KC ) tilde x + B_d d - KB_n n
The whole state space model will then be:
alignl left [matrix{dot x ## dot tilde x ## dot x_i} right ] = left [ matrix{(A-BL) # BL # BLi ## 0 # (A-KC) # 0 ## (DL-C) # -DL # -DLi} right ] left [ matrix{x ## tilde x ## x_i} right ] + left [ matrix{0 # B_d # 0 ## 0 # B_d # - KB_n ## 1 # 0 # -B_n} right ] left [ matrix{r ## d ## n} right ] newline alignl y = left [ matrix{(C-DL) # DL # DLi} right] left [ matrix{x ## tilde x ## x_i} right ] + left [ matrix{0 # 0 # B_n} right] left [ matrix{r ## d ## n} right ]
Because the most important equations are:
alignl dot x = (A-BL)x + BL tilde x + BLi x_i + B_d d newline alignl dot tilde x = ( A - KC ) tilde x + B_d d - KB_n n newline alignl dot x_i = r + ( DL - C )x - DL tilde x - DLi x_i - B_n n newline alignl y = (C - DL)x + DL tilde x + DLi x_i + B_n n